## Slide 1: RISCV CV32E40P CORE VERIFICATION USING UVM & SVA
Team 1
Abdelrahman Yassin Ahmed Khaled Ahmed Ibrahem Esmail Adbelrahman
Mohamed Mohsen
Ziad Ahmed

## Slide 2: Content
RISC-V RV32IM Core Verification
  Motivation to RV32IM
  Design Block Diagram
  UVM Testbench Architecture
  Configurations
  Key components and hierarchy
  Important configuration object
  Environment & Its components
  Agents & their types
  Coverage Collector
  Scoreboard & Checkers
  Simulation Results
  Error Report
  Coverage Closure
  Scripts & Makefiles
This is the main part.

## Slide 3: Motivation to RV32IM
RISC-V is a new instruction-set architecture (ISA) that was originally designed to support computer architecture research and education, but also become a standard free and open architecture for industry implementations.
In the base RV32I ISA, there are four core instruction formats (R/I/S/U). All are a fixed 32 bits in length and must be aligned on a four-byte boundary in memory. There are a further two variants of the instruction formats (B/J) based on the handling of immediates.
RISC-V 32IM Subsets:RV32I (Base Integer): Includes basic arithmetic, logical, load/store, control-flow, and CSR instructions.RV32M (Integer Multiplication/Division Extension): Adds multiply, divide, and remainder operations (e.g., MUL, DIV, REM).

## Slide 4: Design Diagram

## Slide 5: UVM Testbench Architecture

## Slide 6: Configurations

## Slide 7: Config Objects
A Configuration object is passed to the test, then to the environment then the environment passes each agent its own config object
test_config
env_config
id_agent
if_agent
ie_agent
Data_memory agent
Debug_agent
Interrupt_agent

## Slide 8: RegFile Verification Component
Used to have a RegFile mirror which is accessible by multiple components but only one component gets to write in it, To assert the data coherency between different components
LSU Checker (Read only)
ID Checker (Write/Read)
Accessed by

## Slide 9: Sequence Items

## Slide 10: Sequence Items
Base_seq item
Identifies the common things between all of its children sequence items
Can be overridden with its children
ID_seq item
Has the signals which we’re concerned with from the Decode stage input & output signals (Internal)
Registered said signals using obj utilities for comparison, copying, cloning…etc
IF_seq item
Has all the instruction stage input & output signals (Black-Box & White Box Outputs)
Defines Constraints to generate correct instructions upon randomization
EX_seq item
Has the signals which we’re concerned with from the Execute stage input & output signals (Internal)
Registered said signals using obj utilities for comparison, copying, cloning…etc

## Slide 11: Sequence Items
Base_seq item
Identifies the common things between all of its children sequence items
Can be overridden with its children
debug_seq item
Has all the Debug Interface input & output signals
Registered said signals using obj utilities for comparison, copying, cloning…etc
Data_Mem_seq item
Has all the Data_Memory Interface input & output signals
Defines Constraints to generate correct instructions upon randomization
interrupt_seq item
Has all the Interrupt Interface input & output signals
Registered said signals using obj utilities for comparison, copying, cloning…etc

## Slide 12: Sequence Items

## Slide 13: Interfaces

## Slide 14: Interfaces
Data Memory Interface
Has all the Debug Interface input & output signals
Defines a number of Assertions
Debug Interface
Identifies & connects all the input signals to the Instruction debug Interface
Instruction Fetch Interface
Identifies & connects all the input signals to the Instruction Fetch Interface
Defines A number of Assertions
Internal Interface
Identifies & connects all the needed intermediate core signals of the IF, ID, IE, WB stages to the their respective agents
Is handed to the observer module to connect it to the Core’s internal signals
Interrupt Interface
Identifies & connects all the input signals to the Instruction Interrupt Interface

## Slide 15: Environment

## Slide 16: Environment
1
Instantiate
Instantiates all environment components & TLMs
Create
Creates all the instances handles
2
Connect
Connects all TLM ports, exports & implementations
3
Initialize
Initializes all agents using their respective configs
4

## Slide 17: AGENTS

## Slide 18: Agent Types
Agent Types
Active
Reactive
Passive

## Slide 19: Three Types of Reactivity
Reactivity
Using UVM Feedback Implicit Mechanism
@(vif.cb_mon.x); in the driver class
Using an asynchronous or synchronous monitor with TLM to sequencer/sequence

## Slide 20: Reactive Agent
Active Agent
Reset Agent
Gets Configuration from Environment
Creates & Connects to the entire environment
Instantiates:
Monitor
Driver
Sequencer

## Slide 21: Reactive Agent
RE-
Active Agent
Instruction Fetch
Data Memory Slave
Debug Mode
Interrupt Mode
Gets Configuration from Environment
Creates & Connects
Instantiates:
Monitor
Driver
Sequencer

## Slide 22: Passive Agent
Passive
Agent
Instruction Fetch (IF)
Instruction Decode (ID)
Instruction Execution (EX)
Gets Configuration from Environment
Creates & Connects
Instantiates:
Monitor

## Slide 23: if_agent(Reactive)
Driver at 0 time gets all instructions from running sequences.
Driver has internal memory to store all instruction (acts as instruction memory driver)
instr_gnt_i is always 1
Driver has 2 main tasks :
  1. get_instructions : to fill its memory and then trigger fetch_enable_i for 1 clk to start fetching
  2. sample_requests_and_drive: it has 2 subtasks:
    sample_and_send : if a instr_req occurs it samples the address required &
    send the mapped instruction in memory to mailbox
    send_response: get the response from mailbox and sends it on instr_rdata_i
    bus after some random ldelay (valid_delay)
Driver can send B2B & multiple outstanding transactions (based on delay)

## Slide 24: if_agent(Reactive)

## Slide 25: data_memory_if_agent (slave)
Driver consist of 3 parallel taks:
  sample_and_send: responsible to sample any data_req_o & get the response from sequence & push it to mailbox
  send_response: takes responses & drive on DUT based on random value valid_delay
  grant_task:randomizes data_gnt_i to test different scenarios
  Can send B2b ,multiple outstanding transactions

## Slide 26: data_memory_if_agent (slave)

## Slide 27: RST AGENT TLM DIAGRAM
The reset awareness was inspired from The published paper Handling Asynchronous Reset(s) Testing by building reset-awareness into UVM testbench components by Wei Wei Cheong, Katherine Garden, Ana Sanz Carretero which was previewed @DVCON 2021
As shown in the figure, the rst agent monitor class is always waiting for reset assertion, and as soon as it is asserted, the monitor class writes to the uvm_tlm_analysis_port so it reaches every reset_aware component and hence allows them to act accordingly.

## Slide 28: AGENT TLM DIAGRAM
The reset awareness was inspired from The published paper Handling Asynchronous Reset(s) Testing by building reset-awareness into UVM testbench components by Wei Wei Cheong, Katherine Garden, Ana Sanz Carretero which was previewed @DVCON 2021
As shown in the figure, the agent is fully reset aware, every component is connected with uvm_tlm_analysis_imp s to allow it to react to asynchronous reset assertion.
Note: the sequencer in this agent the stop_sequences() function is called within the write function body defined @it, therefore stopping all sequences and calling item_done to all the current running items by the driver.

## Slide 29: Virtual Sequencer

## Slide 30: Virtual Sequencer
Virtual Sequencer
Instantiates the active agent_sequencer & the rst_sequencer so they can be used later to point to the sequencers of the same type inside the virtual sequence and start sequences respectively on them

## Slide 31: TESTS & VIRTUAL SEQUENCES

## Slide 32: Base-Test
Base-Test
Inestantiates the Virtual Sequence
Gets the test_config and uses it to initialize the environment then set the env_cfg to the env
Sets timeout value to the base_vseq to prevent hanging
Starts the base_v_seq on the virtual sequencer

## Slide 33: Tests
R_type_std_test
Overrides bas_vseq with R_type_std_vseq
Checks standard R-type register-to-register instructions like add, sub, and, or, xor, etc.
I_type_std_test
Overrides bas_vseq with I_type_std_vseq
Checks standard I-type instructions like addi, subi, andi, or, xori, etc.
I_type_store_load_test
Overrides bas_vseq with I_type_store_load_vseq
Checks store & load I-type instructions like sb, sh, sw, lb, lh,lw, etc.
I_type_load_test
Overrides bas_vseq with I_type_load_vseq
Checks load I-type instructions like lw, lh, lb, lhu, lbu, etc.

## Slide 34: Tests
Hazard_test
Overrides base_vseq with Hazard_vseq
Checks standard Hazard instructions like read after write, writing != 0 to x0.. etc.
M_Extension_test
Overrides base_vseq with M_Extension_vseq
Checks standard R-type register-to-register instructions like div, divu, mulhsu, or, rem, etc.
S_type_std_test
Overrides base_vseq with S_type_std_vseq
Checks standard S-type instructions like sb, sh, and, sw.
Jalr_test
&
U_type_test
Overrides base_vseq with jalr vseq Overrides base_vseq with U_type_vseq
Checks standard I-type instruction: jalr
Checks standard U-type instructions like lui, auipc.

## Slide 35: Base-vseq
Base-vseq
Inestantiates handles of all the sequences
Inestantiates handles of all the sequencers
Uses `uvm_declare_p_sequencer to create set and casts the p_sequencer to the virtual sequencer which runs the virtual sequence
Hands configurations to sequences if needed

## Slide 36: Virtual Sequences
R_type_std_vseq
Creates all R-Type STD sequences & starts them with the desired pattern
Starts standard R-type register-to-register sequences like and stores seq_items add_seq, sub_seq, and, or_seq, xor_seq, etc.
I_type_std_vseq
Creates all R-Type STD sequences & starts them with the desired pattern
Starts standard I-type sequences like and stores seq_items addi_seq, subi_seq, and, ori_seq, xori_seq, etc.
I_type_store_load_vseq
Creates all R-Type STD sequences & starts them with the desired pattern
Starts standard R-type register-to-register sequences like and stores seq_items sb_seq, sh_seq, and, sw_seq, lb_seq,lh_seq, etc.
I_type_load_vseq
Creates all R-Type STD sequences & starts them with the desired pattern
Starts standard R-type sequences like and stores seq_items lw_seq, lh_seq, and, lb_seq, lhu_seq, etc.

## Slide 37: Virtual Sequences
Hazard_vseq
Creates all Hazard sequences & starts them with the desired pattern
Starts standard Hazard sequences like addi != 0 value to rd, read after write.., etc.
M_Extension_vseq
Creates all M_Extension R-Type sequences & starts them with the desired pattern
Starts standard R-type register-to-register sequence and stores seq_items like div_seq, divu_seq, and, mulhsu_seq, rem_seq, etc.
S_type_std_vseq
Creates all S-Type sequences & starts them with the desired pattern
Starts standard S-type sequences like and stores seq_items sb_seq, sh_seq, sw_seq etc.
Jalr_test
&
U_type_vseq
Creates jalr I-Type sequence & starts it with the desired pattern
Creates all U-Type sequences & starts them with the desired pattern
Starts jalr I-type sequence like and stores seq_items like jalr_seq, etc
Starts standard U-type sequences like and stores seq_items like lui_seq, aui_seq, etc.

## Slide 38: SUBSCRIBER

## Slide 39: Subscriber
Subscriber
Each Subscriber has is connected to the following Agents:
Instruction Interface
Debug Interface
Interrupt Interface
Data Memory Interface
Instruction Fetch Agent
Instruction Decode Agent
Instruction Execution
Receives input stimulus & outputs monitored by the monitor using fork_joined .get() if needed, but only currently uses the ID stage inputs to make sure that the operation has been decoded and is going to be executed
Can be parameterized with test_name, has instance based coverage & static coverage
Is reset aware therefore it is disabled when a reset assertion happens.

## Slide 40: SUBSCRIBER TLM DIAGRAM The reset awareness was inspired from The published paper The reset awareness was inspired from The published paper Handling Asynchronous Reset(s) Testing by building reset-awareness into UVM testbench components by Wei Wei Cheong, Katherine Garden, Ana Sanz Carretero which was previewed @DVCON 2021

## Slide 41: SCOREBOARD

## Slide 42: Checkers
LSU Checker
Checks the outputs of the LSU stage against the expected outputs from the decode stage
Debug intf
checker
Checks the validity of the outputs from the debug interface
Instruction Fetch
Checker (OBI)
Checks the OBI protocol assertion in the Instruction Fetch Interface
EX Checker
Checks the outputs of the Execution stage against the expected outputs which are predicted using the EX stage inputs
ID & Regfile Checker
Checks the Decoding against the outputs of the decoding stage & Regfile against wb signals

## Slide 43: CHECKER EXAMPLE TLM DIAGRAM The hierarchy of this scoreboard is inspired from Clifford Cumming’s OVM-UVM Scoreboards-Fundamental Architectures The reset awareness was inspired from The published paper Handling Asynchronous Reset(s) Testing by building reset-awareness into UVM testbench components by Wei Wei Cheong, Katherine Garden, Ana Sanz Carretero which was previewed @DVCON 2021

## Slide 44: Checker
Checker
Each Active Agent has a Scoreboard:
IF Checker (OBI)
Data Memory Checker (OBI)
ID & Regfile Checker
EX Checker
LSU Checker
Debug Checker
Interrupt Interface
Connects the EXPORTS coming from the environment to the EXPORTS inside the COMPARATOR & the PREDICTOR
Connects the EXPORT Inside the Comparator to the PORT inside the predictor to get the PREDICTED ITEM and compare it to the ACTUAL SAMPLED ITEM
Halts the test using TEST TERMINATION TECHNIQUE used in Clifford Cummings’ OVM & UVM TECHNIQUES FOR TERMINATING TESTS. Raising the objection using the Phase_ready_to_end_phase
Keeps track of Incorrect & Correct comparisons during simulation and displays them in a report

## Slide 45: Predictor
PREDICTOR
Each Scoreboard Agent has a Predictor for:
Instruction Interface
Debug Interface
Interrupt Interface
Data Memory Interface
Instruction Fetch Agent
Instruction Decode Agent
Instruction Execution
Gets the input stimulus sent by the input Monitor using the .get() blocking task from the tlm_analysis_fifo declared within it.
Predicts the Expected Result, assigns it to a seq_item and writes it to the tlm_analysis_port declared within it to the COMPARATOR
Is reset aware, disables all the operations as soon as a reset is detected through the reset TLM

## Slide 46: COMPARATOR
SCOREBOARD
Each Checker has a Comparator:
Instruction Interface
Debug Interface
Interrupt Interface
Data Memory Interface
Instruction Fetch Agent
Instruction Decode Agent
Instruction Execution
Gets the output that was sampled by the output monitor through the uvm_tlm_analysis_fifo using .get() blocking task
Compares the sampled outputs to the expected seq_item sent by the predictor
Is reset aware, disables all the operations as soon as a reset is detected through the reset TLM

## Slide 47: Instruction Fetch

## Slide 48: Instruction Decode

## Slide 49: Waveforms & Simulation Results

## Slide 50: Simulation Results

## Slide 51: Simulation Results

## Slide 52: Simulation Results

## Slide 54: Coverage Closure

## Slide 55: Coverage Examples
Instance – based coverage method
Fixed/Cross – based coverage
method
BODY
Construction
Sampling

## Slide 56: Coverage Closure
- Instance Parameterization according to test name

## Slide 57: Coverage Closure
Naming & Segmentation Faults faced

## Slide 58: Coverage Closure

## Slide 59: Coverage Closure

## Slide 60: Coverage Closure

## Slide 61: Coverage Closure

## Slide 62: Coverage Closure

## Slide 63: Coverage Closure

## Slide 64: Coverage Closure

## Slide 65: Coverage Closure

## Slide 66: Coverage Closure

## Slide 67: Coverage Closure

## Slide 68: Coverage Closure

## Slide 69: Coverage Closure

## Slide 70: Coverage Closure

## Slide 71: Coverage Closure

## Slide 72: Coverage Closure

## Slide 73: Coverage Closure

## Slide 74: CODE COVERAGE

## Slide 75: CODE COVERAGE

## Slide 76: CODE COVERAGE

## Slide 77: Assertions

## Slide 78: Assertions

## Slide 79: Assertions

## Slide 80: Assertions
The above failures are due to the DUT continuously driving instr_req_o even though the instr_gnt_i has been off for a long time.

## Slide 81: Verbosity

## Slide 82: Different Verbosity for Different Debugging Needs
UVM_LOW for Reporting & Checking that the hierarchy is starting correctly & Scoreboard Mismatches
UVM_HIGH for deep-level & case Debugging (usually during the development phase)
UVM_MEDIUM for Correct Cases tracing & Expected behaviour

## Slide 83: Project Path
/home/svgpdv25ahbrahem/RISC_Final/RISV_UVM_FINAL/dv/
Command: ./run.sh

## Slide 84: Conclusions & Future work
Achieved 99% FC but low code coverage as the dut Includes various set of instructions that have not yet been tested (we only test RV32IM)
Add more test scenarios to hit illegal instructions & more corners of DUT & increase code coverage

## Slide 85: Thank You

## Slide 86: Thank You

## Slide 88: Thank You

## Slide 89: Thank You

## Slide 90: Thank You